## Slide 1: Feature Extraction
By Shashank Garikipati on 7/15/2022

## Slide 2: This presentation is organized as follows
Motivations and Definitions
  Motivations
  Basic vehicle definitions
  All about patches
  Metrics
Basic Plotting Functions
Vehicle Collision Detection
  Work zones and obstacles
  Straight path collision detection
  Curved path collision detection
Dataset Point Association
  K-nearest-Neighbor algorithm
  Associated Data Statistics and Modifications

## Slide 3: Motivations and Definitions

## Slide 4: The dynamic and case-specific nature of work zones makes it especially difficult for autonomous vehicles to navigate through them
[morrisseylawfirm.com]
[Freepik.com]
Some objects found in a work zone (not an exhaustive list)

## Slide 5: For this project, we are going to deal with the objects that are commonly found in work zones
Add picture here with all objects from PennDot

## Slide 6: Basic Vehicle Definitions

## Slide 7: We define the following vehicle properties, in body-fixed coordinates
Track width (T)
= Center of Gravity (CG)
CG-front bumper distance (df)
CG-rear bumper distance (dr)

## Slide 8: Sometimes axle-fixed coordinates are used, centered on the rear axle
This is because CG can be difficult to measure, can change, and because most vehicle kinematic motion (low speed) is easily modeled as movement around this point.
[mathworks.com]

## Slide 9: The heading angle is defined as the angle between the positive x axis and the heading (direction the vehicle is facing).
h0
Heading
N
E
W
S

## Slide 10: Slip angle is the angle between the vehicle’s velocity vector and the heading
Slip angle
Vehicle velocity
Heading

## Slide 11: Course over ground is defined as the angle between the positive x axis and the vehicle’s velocity vector
Course over ground
Vehicle velocity
N
E
W
S

## Slide 12: All About Patches

## Slide 13: Patches are used to represent objects that the vehicle can potentially collide into
Patches are represented as [1 x N] struct array in MATLAB
They are primarily defined by the x and y coordinates of their verticies inputted as two [M x 1] vectors for x and y, and a [1 x 3] RBG color vector.

## Slide 14: Patches have directionality – namely the ordering of the vertices defines the surface normal vector.
Anticlockwise ordering means the surface normal points out of the page

## Slide 15: A collidable object is any object that can the vehicle can collide with
[istockphoto.com]
[pragati-trafficsafety.com]
[https://www.pexco.com]
*Not an exhaustive list

## Slide 16: Work zones take various shapes, and tend to have various collidable objects on and near roads
It is important to be able to quickly and accurately detect objects that can potentially collide with the car

## Slide 17: Here is one example of what a zone could look like

## Slide 18: Metrics

## Slide 19: To achieve safe navigation for AVs through a work zone, we define certain measures and metrics. These require geometric functions to calculate intersections, nearest points, etc.
Example of metrics include:
Time to Collision (TTC)
Minimum clearance distance over all objects
Smallest clearance to each object category
If impact, location of impact on the vehicle
If impact, location of impact on the object

## Slide 20: Basic Plotting Functions

## Slide 21: A function in the Feature Extraction library allows users to XY datasets
Function: fcn_Points_plotSetsXY.m
Script: script_test_fcn_Points_plotSetsXY.m
Adapted from fcn_Path_plotTraversalsXY function in the path library
The input to function is an {Mx[Nx2]} cell structure of XY points, where N is the number of points and M is the number of datasets
The function outputs a plot showing the datasets as shown to the left

## Slide 22: Users can create their own XY data using a function in this library
Function: fcn_Points_fillPointSetViaUserInputs.m
Script: script_test_fcn_Path_fillPathViaUserInputs.m
Function was adapted from fcn_Path_fillPathViaUserInputs from the path library
This is a function for the user to click on the figure to generate XY path. Points are collected and plotted until the user double clicks.
The function outputs a plot showing the datasets as shown to the left

## Slide 23: Patches can be easily visualized through the plotPatch function
Function: fcn_Patch_plotPatch.m
Script: script_test_fcn_Patch_plotPatch.m
The input to function is cell structure (Patch array) of X and Y points, where the points are inputted in an anticlockwise manner.

## Slide 24: The library allows users to interactively create patches through color selection and mouse clicks
Function: fcn_Patch_fillPatchArrayViaUserInputs.m

## Slide 25: Sample patches are used to illustrate how patched are implemented in the library
Function: fcn_Patch_fillSamplePatches.m
This function has no inputs. When run, the plot on the left is shown

## Slide 26: During collision detection, Axis Aligned Bounding Boxes (AABB) allow us to quickly filter out “misses” by checking for overlap between bounding boxes
Function: fcn_Patch_determineAABB.m
Script: script_test_fcn_Patch_determineAABB.m
This is faster because we don’t have to compare vertices for each patch
Inputs to this function is a patch array of a cell structure with X and Y points

## Slide 27: An overlap between AABBs doesn’t necessarily mean an intersection is guaranteed
Intersection between patches and AABBs
Intersection between AABBs but not between patches

## Slide 28: Plotting work Zones and Obstacles

## Slide 29: Specific plotting functions have been written for work-zone specific obstacles (Explained in more detail in further slides)
Barrels
Cones
Type III barricades

## Slide 30: Work zones take various shapes, and tend to have various collidable objects on and near roads
The vehicle is shown as the blue box outline and objects are shown as colored in patches

## Slide 31: Common collidable objects found in work zone sites are barrels, which from a top-down view can be modelled as regular octagon patches with radii of 0.2 meters.
[istockphoto.com]
Function: fcn_Patch_fillBarrelAtPoint.m
Script: script_test_fcn_Patch_fillBarrelAtPoint.m

## Slide 32: The user can place barrels at any location and orientation using the fillBarrelAtPoint function
Inputs to the function include [Nx2] coordinates of XY coordinates and [Nx1] vector of orientation points (in radians)
Π/8

## Slide 33: Similarly, Cones can be represented as octagons with radii of 0.16 meters
[indiamart.com]

## Slide 34: Like Barrels, the user can place cones at any location and orientation using the fillConeAtPoint function
Inputs to the function include [Nx2] coordinates of XY coordinates and [Nx1] vector of orientation points (in radians)

## Slide 35: Type III barricades are represented as thin rectangles with a height of 1.5 meters and width of 1.2 meters.
[pexco.com]

## Slide 36: The user can place type III barricades at any location and orientation using the fillType3BarricadeAtPoint function
Π/8
Inputs to the function include [Nx2] coordinates of XY coordinates and [Nx1] vector of orientation points (in radians)

## Slide 37: We have a routine to plot a vehicle as a simple rectangle or with an outline of a vehicle. The details are optional, but useful to disambiguate the travel direction.
Something important to note is that we have to assume the vehicle is a rectangle for the algorithm to work. A collision could be predicted at a location where the vehicle may not exist (e.g. the "carved out corner")

## Slide 38: We also have routines that plot trajectories, given the XY path a vehicle follows. This uses the Path library to calculate offset paths from the vehicle path.
Need to modify function to better visualize left and right lane boundaries

## Slide 39: A more advanced path plotting algorithm uses the arc definitions at each segment, which more precisely captures the vehicle’s envelope

## Slide 40: A function exists also to plot vehicles along a traversal, dropping images of the vehicle onto the traversal periodically to illustrate the motion

## Slide 41: We have plot utilities to plot lane markers. Again, this uses the Path library to calculate offsets from the lane centerline.
*Need to modify function to better look like lane markers

## Slide 42: Several example work zone configurations have been built, and function call can load and plot these configurations.
Matlab representation of work Zone.
Plotted using script_test_fcn_Patch_construction_site.m

## Slide 43
Here is a zoomed in version of the vehicle and near miss points to the channeling device

## Slide 44: Straight Path Collision Detection

## Slide 45: Finding the collision points between obstacles and a vehicle travelling down a straight path
Function: fcn_Patch_checkStraightCollisions.m
Script: script_test_fcn_Patch_checkStraightCollisions.m
Again, something important to note is that we have to assume the vehicle is a rectangle for the algorithm to work. A collision could be predicted at a location where the vehicle may not exist (e.g. the "carved out corner")

## Slide 46: Assumptions before we proceed to solving the problem of straight trajectory collisions
For the sake of demonstration, We assume the collidable object to be in the shape of an arbitrary triangle (this algorithm works for any patch shape)
We assume the car to be approximated as a rectangle bounded by the maximum length and width of the car
Function: fcn_Patch_checkStraightCollisions.m
Script: script_test_fcn_Patch_checkStraightCollisions.m

## Slide 47: The strategy (explained in further details in upcoming slides)
Rotate (about CG) the vehicle and obstacles to point to the x-axis (to turn any situation into a standard problem) – use a rotation matrix
Use polyxpoly (matlab function to find intersection between two polylines) to find points of collision
We then check to see if there are any vertices of the object that lie on this rotated path
We then check to see if there have been any collisions by comparing the vertices and polyxpoly intersection points
collVertexInds = find(abs(rotObst(:,2)) < 1*vehicle.w/2 & rotObst(:,1) > -vehicle.dr);
Function: fcn_Patch_checkStraightCollisions.m
Script: script_test_fcn_Patch_checkStraightCollisions.m

## Slide 48: Rotate (about CG) the vehicle and obstacles to point to the x-axis (to turn any situation into a standard problem) – use a rotation matrix

## Slide 49: Use polyxpoly (matlab function to find intersection between two polylines) to find points of collision
We determine any obstacles that lie within or across the vehicle path on the positive the x-axis between the back of the vehicle (-vehicle.dr) and some large distance (1e6) (this area is given by the red box)
Link to polyxpoly documentation: https://www.mathworks.com/help/map/ref/polyxpoly.html
Potential collision
Potential collision
Potential collision
Potential collision

## Slide 50: We then check to see if there are any vertices of the object that lie on this rotated path
collVertexInds = find(abs(rotObst(:,2)) < 1*vehicle.w/2 & rotObst(:,1) > -vehicle.dr);
Checking within the width of the vehicle
Checking between x-axis between back of vehicle and come large distance

## Slide 51: We then check to see if there have been any collisions by comparing the points we obtained before
If there is a collision, we compare whether the vertex was closer or polyxpoly point is closer. Which ever point is closer is the collision point.
If there is no collision, we try to find the minimum clearance and location of this on the obstacle.
Closest point -> point of collision

## Slide 52: Once this point is obtained, we rotate and translate it back to the original coordinate space
*
*
Collision point

## Slide 53: If there is no collision at all, we determine the clearance of all the vertices on the obstacle to determine the location of the “near miss”
The closest point ( minimum clearance is the point of near miss)
Near miss

## Slide 54: There are several test cases that the algorithm can encounter, which can be found in script_test_fcn_Patch_checkStraightCollisions.m
Collision with right edge
Collision with left edge

## Slide 55
Collision with vertex
Collision with multiple objects’ vertex

## Slide 56: The algorithm displays the location of the minimum clearances on the figure as near misses
Near miss
Multiple near misses

## Slide 57: We can also have these different test cases plotted as a single scenario

## Slide 58: Curved Path Collision Detection

## Slide 59: Finding the collision between a objects and a vehicle travelling down a curved patch
Something important to note is that a straight path is considered to be a curved path with an infinite radius, so any path can be treated as a curved path.
However, we consider the straight path to be a special case and use fcn_Patch_checkStraightCollisions.m for that case
Function: fcn_Patch_checkCollisions.m
Script: script_test_fcn_Patch_checkCollisions.m

## Slide 60: The strategy to determine circular trajectory collisions (explained in further details in upcoming slides)
Define pertinent radii and calculate center of path radius circle
Convert from vehicle body coordinates to inertial coordinates using a rotation matrix
Checking to find intersection points between vehicle vertex and object edge
Checking to find intersection points object vertex and vehicle edge
Checking for collision by comparing obtained intersection points or calculating near misses
Function: fcn_Patch_checkCollisions.m
Script: script_test_fcn_Patch_checkCollisions.m

## Slide 61: Vehicle trajectory for a curved path is defined by several pertinent radii

## Slide 62: They are calculated as follows:
CG (circle) and CG path (black dash-dot line)
Front left and front right corner paths (gray lines)
Maximum clearance radius (blue line)
Minimum clearance radius (red line)
a

## Slide 63: We first use a function in the library to find these pertinent radii of the circular trajectory that the vehicle can clear without collision
Function: fcn_Patch_CalcCircularTrajectoryGeometry.m
Script: script_test_fcn_Patch_CalcCircularTrajectoryGeometry.m
It also returns the tangent point (given by the *)
of the inner limiting radii

## Slide 64: Object vertices radii are calculated with respect to the center of trajectory of the vehicle
Center of vehicle
trajectory
v1
v2
v5
v4
v3
v1 radius

## Slide 65: Then, we calculate the angle for each bounding point on the car with respect to the center of the circular trajectory at the start point
Center of trajectory
y1
LR
LF
RF
RR
x1
theta
For instance, to calculate the angle for LF:
Theta = tan-1(y1/x1)
LF – Left front
RF – Right front
LR – Left rear
RR – Right rear
CoG – Center of gravity
Bounding points
of the car
Circular trajectory
COG

## Slide 66: We repeat a similar calculation to obtain angles for the vertices of all the obstacles
Center of vehicle
trajectory
v1
v2
v5
v4
v3
theta

## Slide 67: The section of code that checks hits and misses is split into three sub-sections.
Section 1: vehicle vertex to object edge checks
Section 2: object vertex to vehicle edge checks
Section 3: first collision selection, or clearance calculation

## Slide 68: We compare the left and right front vehicle vertices to each of the object edges to check for collision using a function in the geometry library
Section 1
LR
LF
RF
RR
COG
Edge 1
Edge 2
Edge 3
Front vertices of vehicle

## Slide 69: The function works by comparing the circles formed by each of the vehicle’s vertices to the lines formed by each edge of the obstacle
Center of trajectory
LR
LF
RF
RR
COG
Hit
Hit
Hit
Hit
Function from geometry library used: fcn_geometry_findIntersectionLineSegmentWithCircle
The function returns the angle and point of intersection with respect to the x-axis with the center of the circle trajectory being the origin
Check geometry library for more information about the function
angle
Section 1

## Slide 70: A special kind of collision could occur when the edge spans the max radius with vertex outside of outer front track radius
This case is tackled in a similar method to above
The circle formed by the radius of the tangent point (indicated by the red dot) is compared to vertices of the object using fcn_geometry_findIntersectionLineSegmentWithCircle in the geometry library

## Slide 71: In section 2, we start off by determining whether a vertex falls into the vehicle’s trajectory
This is achieved by first comparing the vertex’s radii to the vehicle’s minimum and maximum radii
Secondly, we check to see that if lies in between the trajectory of the front edge specifically
if vertexRadii(vertexInd) > Rmin && vertexRadii(vertexInd) < Rmax
% First, check the front of the vehicle, which will have a
% collision if the obstacle vertex lies between the radii of
% the LF and RF points. But need to check both cases since
% the ordering of the radii magnitude will change depending on
% the direction of travel.
if (vertexRadii(vertexInd) >= R_LF && vertexRadii(vertexInd) <= R_RF) || (vertexRadii(vertexInd) <= R_LF && … ...vertexRadii(vertexInd) >= R_RF)
% If the vertex has an intersection with the front of the
% vehicle, calculate the intersections

## Slide 72: If a vertex does exist on the trajectory , We compare the object vertices to each of the vehicle’s front edge to check for collision
Center of trajectory
LR
LF
RF
RR
COG
Hit
angle
Repeat for each objects’ vertex that lie in the trajectory of the vehicle to find and store angle and point of intersection
Section 2

## Slide 73: A special “sideswipe” could occur, where the object’s vertex collides with one of the two vehicle side edges
This case is tackled in a similar method to above
The circle formed by the radius of the tangent point (indicated by the red dot) is compared to vertices of the object using fcn_geometry_findIntersectionLineSegmentWithCircle in the geometry library
Section 2

## Slide 74: Sideswipe collisions occur regularly in real life resulting in damages to the side of the vehicle
[www.randyakin.com]
Section 2

## Slide 75: Once the first two checks are complete, we consider the case where no intersections were detected for an object
Section 3

## Slide 76: The closest point on the object to the vehicle’s trajectory is the point of near miss
Closest point =>
Section 3

## Slide 77: There are two possible scenario’s we need to consider to determine this point
Section 3

## Slide 78: For case 1, The “near miss” point on the obstacle can lie anywhere on the edge depending on the situation, so we use alpha to find this point
Alpha is a ratio defined as:
Alpha = (pa(x) – pc(x))*(pb(x) – pa(x)) + (pa(x) – pc(x))*(pb(x) – pa(x))
((pb(x)-pa(x))2 + (pb(y)-pa(y))2
If 0 < alpha < 1, the intersection lies on the edge and can be computed as : Intersection point = pa + alpha*(pb – pa)
If alpha does not lie within this range, Intersection point = pa because it is closer of the two points
Section 3

## Slide 79: We determine point pa and pb( the two closest outer vertex points) by finding the minimum distance from these points to the max radius
The distances can be easily computer as:
d = Radius(pa) – Rmax
The points with the shortest two distances will be pa and pb
Section 3

## Slide 80: For case 2, The “near miss” point is simply the closest vertex to the minimum that can be easily computed by comparing distances like case 1
The distances can be easily computer as follows:
d = Rmin - Radius(pa)
The points with the shortest distances will be pa
pa
Section 3

## Slide 81
There are numerous possible collision/near miss possibilities, which are summarized in the table below
 | Front of Car | Inside of Car | Outside of Car
Vertex within track width | Direct calculation of vertex angle relative to center | N/A | N/A
Vertex between inside front corner and min radius | N/A | Calculate distance ahead of CG for collision then offset from vertex angle | N/A
Vertex between outside front corner and max radius | N/A | N/A | Calculate distance behind CG for collision then offset from vertex angle
Edge entirely within track width | Handled by vertex checks | N/A | N/A
Edge between min radius and track width | Handled by vertex check if track width vertex comes first | Circle/edge intersection check with inside front | N/A
Edge between max radius and track width | Handled by vertex check if track width vertex comes first | N/A | Circle/edge intersection check with outside front
Edge spans the track width but vertices within min and max radii | N/A unless edge is perfectly parallel to front of car | Circle/edge intersection check with inside front | Circle/edge intersection check with outside front
Edge spans min and max radii | N/A unless edge is perfectly parallel to front of car | Circle/edge intersection check with inside front | Circle/edge intersection check with outside front
Edge spans max radius with vertex outside of outer front track radius | N/A | N/A | Circle/edge intersection check with outside rear OR vertex check behind CG (depends on edge angle)
Edge spans min radius with vertex outside of inner front track radius | N/A | Vertex check ahead of CG | N/A
Vertices outside max/min radii (near miss) | N/A | Determine point with minimum difference from CG radius by vertices | Determine point with minimum difference from CG radius by vertices and nearest point on edges.
Cases are shown with images in upcoming slides

## Slide 82: Vertex/vertices is within track width

## Slide 83: Vertex is between inside front corner and minimum radius

## Slide 84: Vertex is between outside front corner and maximum radius

## Slide 85: Edge is entirely within track width

## Slide 86: Edge is between minimum radius and track width

## Slide 87: Edge is between maximum radius and track width

## Slide 88: Edge spans the track width but vertices within min and maximum radii

## Slide 89: Edge spans the minimum and maximum radii

## Slide 90: Edge spans max radius with vertex outside of outer front track radius

## Slide 91: Edge spans min radius with vertex outside of inner front track radius

## Slide 92: Vertices are outside maximum/minimum radii (near miss)

## Slide 93: K-Nearest-Neighbor Algorithm

## Slide 94: In a work zone, objects such as cones regularly move around their original positions
Orange circle represents cone from top-down view

## Slide 95: In a work zone, associating XY points would enable us to determine how much cones and other such objects move
Plot showing association of points

## Slide 96: X,Y points from two different datasets can be paired as an application of machine leaning (k-nearest neighbor algorithm)
Zoomed in version of the plot on the previous slide
Function: fcn_Points_pairXYdata.m
Script: script_test_fcn_Points_pairXYdata.m

## Slide 97: In this problem, we want to associate X,Y data points in one data set (a map, for example) with X,Y data points in another data set
The data sets are not assumed to be sorted or have the same number of points.
A graphical depiction is given for two data sets here:
Data Set B
Data Set A

## Slide 98: Association of XY points to XY points
The data sets are likely to have some points that are “mutual matches” where a pair of points in set A and set B are each the closest point to the point in the opposing data set.
The data sets are also likely to have points that do not have a close match once all of the mutual matches have been assigned.
Data Set B
Data Set A

## Slide 99: Nearest-neighbor or k-Nearest-Neighbor (kNN) searches are well-researched machine learning algorithms that can help determine mutual matches
  MATLAB implementation: [idx, dist] = knnsearch(datasetA, datasetB);
  The kNN search will return a vector of indices that indicate the nearest neighbor in datasetA to each point in datasetB.
  This can be modified to return a matrix of multiple (k) nearest neighbors for each point in datasetB.
  https://www.mathworks.com/help/stats/knnsearch.html
Requires: Statistics and Machine Learning Toolbox

## Slide 100: There may be points in set A that are the closest for multiple points in set B, or points that are never identified as a nearest neighbor.
Not a
neighbor
Duplicate
neighbor
Data Set B
Data Set A

## Slide 101: How the algorithm works
  Apply 1NN search to find the nearest neighbors in both directions
  Compare returned indices to determine which points have mutual matches
Data Set B
Data Set A

## Slide 102: How the algorithm works (continued)
  Check each mutual match the distance is less than a radial limit
  Reorganize (or copy) the matched points in Data Set A and Data Set B into a matrix where each row contains the X and Y coordinates of the two points
  Optionally, append each of the unmatched points in Data Set A with padding in the last two columns since there aren’t matches in Data Set B
  Optionally, append each of the unmatched points in Data Set B with padding in the first two columns since there aren’t matches in Data Set A
Data Set B
Data Set A

## Slide 103: For example, here are two repeated but slightly different locations of cones that are correctly associated with each other.
Here, we are checking to see if the cones are within 1 m of each other
Script: script_test_fcn_Points_addRadialNoise.m

## Slide 104: Here’s an example where the cone has moved cone has moved outside the user-specified radius., so is not associated with itself over time.
We are still limiting the max association distance to 1 unit, but since the two cones are further apart than this, it is not longer associated.
Script: script_test_fcn_Points_addRadialNoise.m

## Slide 105: Associated Data Statistics and Modifications

## Slide 106: It is useful to have some statistics for points in datasets that have been associated with each other
RMS Error: the RMS distances associated with the point-to-point match errors
Variance Error: the variance in the point-to-point match error distances
Mean Shift: the [X Y] shift that would cause the centroids of the two data sets to match
A function in the library helps us do this
Function: fcn_Points_calcPairStatistics.m
Script: script_test_fcn_Points_calcPairStatistics.m

## Slide 107: Another function allows us to modify the statistics of datasets by adjusting XY points using polar projections. This is illustrated by 1000 biases of the original data.
Function: fcn_Points_adjustPointSetStatistics.m
Script: script_test_fcn_Points_adjustPointSetStatistics.m
Datasets can be modified using three methods:
Systematic
Mean Noise
Variance Noise

## Slide 108: A modification on a larger scale would look like this:
Systematic bias of 0.1 on both x and y
Variance noise of 0.1 on x
1-D gaussian noise
Variance noise of 0.1 on x and y
2-D gaussian noise

## Slide 109: addRadialNoise is a function that adds random noise in a radial manner
For a point centered at [0,0], here is noise added radially with a radius of 0.5 units. The function was iterated 300 times to show the circle of noise
Function: fcn_Points_addRadialNoise.m
Script: script_test_fcn_Points_addRadialNoise.m

## Slide 110: Here’s an example where many cones are measured twice. All are moved, some disappear, and some appear in the 2nd measurement.
1st measurement
2nd measurement
Green circles => measured twice. Red circles if measured in set A but missing in set B, and blue circles if measured in Set B but missing in set A.

## Slide 111: References
https://www.freepik.com/free-vector/set-construction-site-objects_27285642.htm
https://www.istockphoto.com/photos/road-construction-barrels
https://www.wired.com/2017/02/self-driving-cars-cant-even-construction-zones/
https://www.randyakin.com/blog/2019/12/29/sideswipe-car-accidents-203205
https://www.pexco.com/traffic/products/barricade-products/
http://www.pragati-trafficsafety.com/Safety-Barricades-and-Cones/Flexible-Traffic-Cone
https://www.istockphoto.com/search/2/image?phrase=road+construction+barrels
https://www.mathworks.com/help/driving/ug/coordinate-systems.html

## Slide 113
Case 2:
Object lies inside Rmin
Rmax
Rmin
Case 2 closest point

## Slide 114
Rmax
Rmin
Case 1 closest point
Case 1:
Object lies outside Rmax