## Slide 1: Detecting Collisions
By Shashank Garikipati on 6/28/2022

## Slide 2: This presentation is organized as follows
Motivations
Dataset point association
  Basic dataset plotting functions
  K-nearest-Neighbor algorithm
  Associated Data Statistics and Modifications
All about patches
Vehicle collision detection
  Basic vehicle definitions
  Construction zones and obstacles
  Straight path collision detection
  Curved path collision detection

## Slide 3: Motivations

## Slide 4: The dynamic and case-specific nature of construction work zones makes it especially difficult for autonomous vehicles to navigate through them
[morrisseylawfirm.com]
[Freepik.com]
Some objects found in a work zone (not an exhaustive list)

## Slide 5: Construction work zones take various shapes, and tend to have various collidable objects on and near roads
It is important to be able to quickly and accurately detect objects that can potentially collide with the car

## Slide 6: Basic Dataset Plotting Functions

## Slide 7: A function in the Feature Extraction library allows users to XY datasets
Function: fcn_Points_plotSetsXY.m
Script: script_test_fcn_Points_plotSetsXY.m
Adapted from fcn_Path_plotTraversalsXY function in the path library

## Slide 8: Users can create their own XY data using a function in this library
Function: fcn_Points_fillPointSetViaUserInputs.m
Script: script_test_fcn_Path_fillPathViaUserInputs.m
Function was adapted from fcn_Path_fillPathViaUserInputs from the path library
This is a function for the user to click on the figure to generate XY path. Points are collected and plotted until the user double clicks.

## Slide 9: K-Nearest-Neighbor Algorithm

## Slide 10: Associating XY points in one dataset (A map) to another dataset (waypoints) is a useful tool when working with construction zones
Plot showing association of points

## Slide 11: X,Y points from two different datasets can be paired as an application of machine leaning (k-nearest neighbor algorithm)
Zoomed in version of the plot on the previous slide
Function: fcn_Points_pairXYdata.m
Script: script_test_fcn_Points_pairXYdata.m

## Slide 12: In this problem, we want to associate X,Y data points in one data set (a map, for example) with X,Y data points in another data set
The data sets are not assumed to be sorted or have the same number of points.
A graphical depiction is given for two data sets here:
Data Set B
Data Set A

## Slide 13: Association of XY points to XY points
The data sets are likely to have some points that are “mutual matches” where a pair of points in set A and set B are each the closest point to the point in the opposing data set.
The data sets are also likely to have points that do not have a close match once all of the mutual matches have been assigned.
Data Set B
Data Set A

## Slide 14: Nearest-neighbor or k-nearest-neighbor (kNN) searches are well-researched machine learning algorithms that can help determine mutual matches
  MATLAB implementation: [idx, dist] = knnsearch(datasetA, datasetB);
  The kNN search will return a vector of indices that indicate the nearest neighbor in datasetA to each point in datasetB.
  This can be modified to return a matrix of multiple (k) nearest neighbors for each point in datasetB.
  https://www.mathworks.com/help/stats/knnsearch.html
Requires: Statistics and Machine Learning Toolbox

## Slide 15: There may be points in set A that are the closest for multiple points in set B, or points that are never identified as a nearest neighbor.
Data Set B
Data Set A
Not a
neighbor
Duplicate
neighbor

## Slide 16: How the algorithm works
  Apply 1NN search to find the nearest neighbors in both directions
  Compare returned indices to determine which points have mutual matches
Data Set B
Data Set A
Data Set B
Data Set A
Data Set B
Data Set A
Data Set B
Data Set A

## Slide 17: How the algorithm works (continued)
  Check each mutual match the distance is less than a radial limit
  Reorganize (or copy) the matched points in Data Set A and Data Set B into a matrix where each row contains the X and Y coordinates of the two points
  Optionally, append each of the unmatched points in Data Set A with padding in the last two columns since there aren’t matches in Data Set B
  Optionally, append each of the unmatched points in Data Set B with padding in the first two columns since there aren’t matches in Data Set A
Data Set B
Data Set A
Data Set B
Data Set A

## Slide 18: Associated Data Statistics and Modifications

## Slide 19: It is useful to have some statistics for points in datasets that have been associated with each other
RMS Error: the RMS distances associated with the point-to-point match errors
Variance Error: the variance in the point-to-point match error distances
Mean Shift: the [X Y] shift that would cause the centroids of the two data sets to match
A function in the library helps us do this
Function: fcn_Points_calcPairStatistics.m
Script: script_test_fcn_Points_calcPairStatistics.m

## Slide 20: Another function allows us to modify the statistics of datasets by adjusting XY points
Function: fcn_Points_adjustPointSetStatistics.m
Script: script_test_fcn_Points_adjustPointSetStatistics.m

## Slide 21: Patches are used to represent objects that the vehicle can potentially collide into
Patches are represented as [1 x N] struct array in MATLAB
They are primarily defined by the x and y coordinates of their verticies inputted as two [M x 1] vectors for x and y, and a [1 x 3] RBG color vector.

## Slide 22: Sample patches are used to illustrate how patched are implemented in the library
Function: fcn_Patch_fillSamplePatches.m
Script: No script yet

## Slide 23: These patches can be easily visualized
Function: fcn_Patch_plotPatch.m
Script: script_test_fcn_Patch_plotPatch.m

## Slide 24: The library allows users to interactively create patches through color selection and mouse clicks
Function: fcn_Patch_fillPatchArrayViaUserInputs.m
Script: No script yet

## Slide 25: Axis Aligned Bounding Boxes (AABB), which are useful when working with collision detection, can be determined for each of the patches
Function: fcn_Patch_determineAABB.m
Script: script_test_fcn_Patch_determineAABB.m

## Slide 26: Basic Vehicle definitions

## Slide 27: We define the following vehicle properties
Body width
= Center of Gravity (CG)
CG-front bumper distance (df)
CG-rear bumper distance (dr)

## Slide 28: The heading angle is defined as the angle between the positive x axis and the heading (direction the vehicle is facing).
h0
Heading

## Slide 29: Slip angle is the angle between the vehicle’s velocity vector and the heading
Slip angle
Vehicle velocity
Heading

## Slide 30: The heading angle is defined as the angle between the positive x axis and the vehicle’s velocity vector
Course over ground
Vehicle velocity

## Slide 31: Construction Zones and Obstacles

## Slide 32: Construction work zones take various shapes, and tend to have various collidable objects on and near roads

## Slide 33: Common collidable objects found in construction sites are barrels, which from a top-down view can be modelled as regular octagon patches.
[istockphoto.com]
Function: fcn_Patch_fillBarrelAtPoint.m
Script: script_test_fcn_Patch_fillBarrelAtPoint.m

## Slide 34: Straight Path Collision Detection

## Slide 35: Finding the collision points between obstacles and a vehicle travelling down a straight path
Function: fcn_Patch_checkStraightCollisions.m
Script: script_test_fcn_Patch_checkStraightCollisions.m

## Slide 36: Important assumptions before we proceed to tackling the problem
We assume the collidable object to be in the shape of an arbitrary triangle
We assume the car to be approximated as a rectangle bounded by the maximum length and width of the car

## Slide 37: The strategy (explained in further details in upcoming slides)
Rotate (about CG) the vehicle and obstacles to point to the x-axis (to turn any situation into a standard problem) – use a rotation matrix
Use polyxpoly (matlab function to find intersection between two polylines) to find points of collision
We then check to see if there are any vertices of the object that lie on this rotated path
We then check to see if there have been any collisions by comparing the vertices and polyxpoly intersection points
collVertexInds = find(abs(rotObst(:,2)) < 1*vehicle.w/2 & rotObst(:,1) > -vehicle.dr);

## Slide 38: Rotate (about CG) the vehicle and obstacles to point to the x-axis (to turn any situation into a standard problem) – use a rotation matrix

## Slide 39: Use polyxpoly (matlab function to find intersection between two polylines) to find points of collision
We determine any obstacles that lie within or across the vehicle path on the positive the x-axis between the back of the vehicle (-vehicle.dr) and some large distance (1e6) (this area is given by the red box)
Link to polyxpoly documentation: https://www.mathworks.com/help/map/ref/polyxpoly.html
Potential collision
Potential collision
Potential collision
Potential collision

## Slide 40: We then check to see if there are any vertices of the object that lie on this rotated path
collVertexInds = find(abs(rotObst(:,2)) < 1*vehicle.w/2 & rotObst(:,1) > -vehicle.dr);
Checking within the width of the vehicle
Checking between x-axis between back of vehicle and come large distance

## Slide 41: We then check to see if there have been any collisions by comparing the points we obtained before
If there is a collision, we compare whether the vertex was closer or polyxpoly point is closer. Which ever point is closer is the collision point.
If there is no collision, we try to find the minimum clearance and location of this on the obstacle.
Closest point -> point of collision

## Slide 42: Once this point is obtained, we rotate and translate it back to the original coordinate space
*
*
Collision point

## Slide 43: There are several test cases that the algorithm can encounter
Collision with right edge
Collision with left edge
Collision with multiple objects’ edges

## Slide 44
Collision with vertex
Collision with multiple objects’ vertex

## Slide 45: The algorithm displays the location of the minimum clearances on the figure as near misses

## Slide 46: We can also have these different test cases plotted as a single scenario

## Slide 47: Curved Path Collision Detection

## Slide 48: Finding the collision between a objects and a vehicle travelling down a curved patch
Something important to note is that a straight path is considered to be a curved path with an infinite radius, so any path can be treated as a curved path.
However, we consider the straight path to be a special case and use fcn_Patch_checkStraightCollisions.m for that case
Function: fcn_Patch_checkCollisions.m
Script: script_test_fcn_Patch_checkCollisions.m

## Slide 49: The strategy (explained in further details in upcoming slides)
Define pertinent radii and calculate center of path radius circle
Convert from vehicle body coordinates to inertial coordinates using a rotation matrix
Checking to find intersection points between vehicle vertex and object edge
Checking to find intersection points object vertex and vehicle edge
Checking for collision by comparing obtained intersection points or calculating near misses

## Slide 50: Vehicle trajectory for a curved path is defined by several pertinent radii

## Slide 51: They are calculated as follows:
CG (circle) and CG path (black dash-dot line)
Front left and front right corner paths (gray lines)
Maximum clearance radius (blue line)
Minimum clearance radius (red line)
a

## Slide 52: We first use a function in the library to find these pertinent radii of the circular trajectory that the vehicle can clear without collision
Function: fcn_Patch_CalcCircularTrajectoryGeometry.m
Script: script_test_fcn_Patch_CalcCircularTrajectoryGeometry.m
It also returns the tangent point (given by the *)
of the inner limiting radii

## Slide 53: Object vertices radii are calculated with respect to the center of trajectory of the vehicle
Center of vehicle
trajectory
v1
v2
v5
v4
v3
v1 radius

## Slide 54: Then, we calculate the angle for each bounding point on the car with respect to the center of the circular trajectory at the start point
Center of trajectory
y1
LR
LF
RF
RR
x1
theta
For instance, to calculate the angle for LF:
Theta = tan-1(y1/x1)
LF – Left front
RF – Right front
LR – Left rear
RR – Right rear
CoG – Center of gravity
Bounding points
of the car
Circular trajectory
COG

## Slide 55: We repeat a similar calculation to obtain angles for the vertices of all the obstacles
Center of vehicle
trajectory
v1
v2
v5
v4
v3
theta

## Slide 56: The section of code that checks hits and misses is split into three sub-sections.
Section 1: vehicle vertex to object edge checks
Section 2: object vertex to vehicle edge checks
Section 3: first collision selection, or clearance calculation

## Slide 57: We compare the left and right front vehicle vertices to each of the object edges to check for collision using a function in the geometry library
Section 1
LR
LF
RF
RR
COG
Edge 1
Edge 2
Edge 3
Front vertices of vehicle

## Slide 58: The function works by comparing the circles formed by each of the vehicle’s vertices to the lines formed by each edge of the obstacle
Center of trajectory
LR
LF
RF
RR
COG
Hit
Hit
Hit
Hit
Function from geometry library used: fcn_geometry_findIntersectionLineSegmentWithCircle
The function returns the angle and point of intersection with respect to the x-axis with the center of the circle trajectory being the origin
Check geometry library for more information about the function
angle
Section 1

## Slide 59: A special kind of collision could occur when the edge spans the max radius with vertex outside of outer front track radius
This case is tackled in a similar method to above
The circle formed by the radius of the tangent point (indicated by the red dot) is compared to vertices of the object using fcn_geometry_findIntersectionLineSegmentWithCircle in the geometry library

## Slide 60: In section 2, we start off by determining whether a vertex falls into the vehicle’s trajectory
This is achieved by first comparing the vertex’s radii to the vehicle’s minimum and maximum radii
Secondly, we check to see that if lies in between the trajectory of the front edge specifically
if vertexRadii(vertexInd) > Rmin && vertexRadii(vertexInd) < Rmax
% First, check the front of the vehicle, which will have a
% collision if the obstacle vertex lies between the radii of
% the LF and RF points. But need to check both cases since
% the ordering of the radii magnitude will change depending on
% the direction of travel.
if (vertexRadii(vertexInd) >= R_LF && vertexRadii(vertexInd) <= R_RF) || (vertexRadii(vertexInd) <= R_LF && … ...vertexRadii(vertexInd) >= R_RF)
% If the vertex has an intersection with the front of the
% vehicle, calculate the intersections

## Slide 61: If a vertex does exist on the trajectory , We compare the object vertices to each of the vehicle’s front edge to check for collision
Center of trajectory
LR
LF
RF
RR
COG
Hit
angle
Repeat for each objects’ vertex that lie in the trajectory of the vehicle to find and store angle and point of intersection
Section 2

## Slide 62: A special “sideswipe” could occur, where the object’s vertex collides with one of the two vehicle side edges
This case is tackled in a similar method to above
The circle formed by the radius of the tangent point (indicated by the red dot) is compared to vertices of the object using fcn_geometry_findIntersectionLineSegmentWithCircle in the geometry library
Section 2

## Slide 63: Sideswipe collisions occur regularly in real life resulting in damages to the side of the vehicle
[www.randyakin.com]
Section 2

## Slide 64: Once the first two checks are complete, we consider the case where no intersections were detected for an object
Section 3

## Slide 65: The closest point on the object to the vehicle’s trajectory is the point of near miss
Closest point =>
Section 3

## Slide 66: There are two possible scenario’s we need to consider to determine this point
Section 3

## Slide 67: For case 1, The “near miss” point on the obstacle can lie anywhere on the edge depending on the situation, so we use alpha to find this point
Alpha is a ratio defined as:
Alpha = (pa(x) – pc(x))*(pb(x) – pa(x)) + (pa(x) – pc(x))*(pb(x) – pa(x))
((pb(x)-pa(x))2 + (pb(y)-pa(y))2
If 0 < alpha < 1, the intersection lies on the edge and can be computed as : Intersection point = pa + alpha*(pb – pa)
If alpha does not lie within this range, Intersection point = pa because it is closer of the two points
Section 3

## Slide 68: We determine point pa and pb( the two closest outer vertex points) by finding the minimum distance from these points to the max radius
The distances can be easily computer as:
d = Radius(pa) – Rmax
The points with the shortest two distances will be pa and pb
Section 3

## Slide 69: For case 2, The “near miss” point is simply the closest vertex to the minimum that can be easily computed by comparing distances like case 1
The distances can be easily computer as follows:
d = Rmin - Radius(pa)
The points with the shortest distances will be pa
pa
Section 3

## Slide 70
There are numerous possible collision/near miss possibilities, which are summarized in the table below
 | Front of Car | Inside of Car | Outside of Car
Vertex within track width | Direct calculation of vertex angle relative to center | N/A | N/A
Vertex between inside front corner and min radius | N/A | Calculate distance ahead of CG for collision then offset from vertex angle | N/A
Vertex between outside front corner and max radius | N/A | N/A | Calculate distance behind CG for collision then offset from vertex angle
Edge entirely within track width | Handled by vertex checks | N/A | N/A
Edge between min radius and track width | Handled by vertex check if track width vertex comes first | Circle/edge intersection check with inside front | N/A
Edge between max radius and track width | Handled by vertex check if track width vertex comes first | N/A | Circle/edge intersection check with outside front
Edge spans the track width but vertices within min and max radii | N/A unless edge is perfectly parallel to front of car | Circle/edge intersection check with inside front | Circle/edge intersection check with outside front
Edge spans min and max radii | N/A unless edge is perfectly parallel to front of car | Circle/edge intersection check with inside front | Circle/edge intersection check with outside front
Edge spans max radius with vertex outside of outer front track radius | N/A | N/A | Circle/edge intersection check with outside rear OR vertex check behind CG (depends on edge angle)
Edge spans min radius with vertex outside of inner front track radius | N/A | Vertex check ahead of CG | N/A
Vertices outside max/min radii (near miss) | N/A | Determine point with minimum difference from CG radius by vertices | Determine point with minimum difference from CG radius by vertices and nearest point on edges.
Cases are shown with images in upcoming slides

## Slide 71: Vertex/vertices is within track width

## Slide 72: Vertex is between inside front corner and minimum radius

## Slide 73: Vertex is between outside front corner and maximum radius

## Slide 74: Edge is entirely within track width

## Slide 75: Edge is between minimum radius and track width

## Slide 76: Edge is between maximum radius and track width

## Slide 77: Edge spans the track width but vertices within min and maximum radii

## Slide 78: Edge spans the minimum and maximum radii

## Slide 79: Edge spans max radius with vertex outside of outer front track radius

## Slide 80: Edge spans min radius with vertex outside of inner front track radius

## Slide 81: Vertices are outside maximum/minimum radii (near miss)

## Slide 83
Case 2:
Object lies inside Rmin
Rmax
Rmin
Case 2 closest point

## Slide 84
Rmax
Rmin
Case 1 closest point
Case 1:
Object lies outside Rmax

## Slide 85: References
https://www.freepik.com/free-vector/set-construction-site-objects_27285642.htm
https://www.istockphoto.com/photos/road-construction-barrels
https://www.wired.com/2017/02/self-driving-cars-cant-even-construction-zones/
https://www.randyakin.com/blog/2019/12/29/sideswipe-car-accidents-203205