## Slide 1: Detecting Collisions
By Shashank Garikipati on 6/28/2022

## Slide 2: This presentation is organized as follows
Motivations
Dataset point association
  Basic dataset plotting functions
  K-nearest-Neighbor algorithm
  Associated Data Statistics and Modifications
All about patches
Vehicle collision detection
  Basic vehicle definitions
  Construction zones and obstacles
  Straight path collision detection
  Curved path collision detection

## Slide 3: Motivations

## Slide 4: The dynamic and case-specific nature of construction work zones makes it especially difficult for autonomous vehicles to navigate through them
[morrisseylawfirm.com]
[Freepik.com]
Some objects found in a work zone (not an exhaustive list)

## Slide 5: Construction work zones take various shapes, and tend to have various collidable objects on and near roads
It is important to be able to quickly and accurately detect objects that can potentially collide into the car

## Slide 6: Basic Dataset Plotting Functions

## Slide 7: A function in the Feature Extraction library allows users to XY datasets
Function: fcn_Points_plotSetsXY.m
Script: script_test_fcn_Points_plotSetsXY.m
Adapted from fcn_Path_plotTraversalsXY function in the path library

## Slide 8: Users can create their own XY data using a function in this library
Function: fcn_Points_fillPointSetViaUserInputs.m
Script: script_test_fcn_Path_fillPathViaUserInputs.m
Function was adapted from fcn_Path_fillPathViaUserInputs from the path library
This is a function for the user to click on the figure to generate XY path. Points are collected and plotted until the user double clicks.

## Slide 9: K-Nearest-Neighbor Algorithm

## Slide 10: Associating XY points in one dataset (A map) to another dataset (waypoints) is a useful tool when working with construction zones
Plot showing association of points

## Slide 11: X,Y points from two different datasets can be paired as an application of machine leaning (k-nearest neighbor algorithm)
Zoomed in version of the plot on the previous slide
Function: fcn_Points_pairXYdata.m
Script: script_test_fcn_Points_pairXYdata.m

## Slide 12: In this problem, we want to associate X,Y data points in one data set (a map, for example) with X,Y data points in another data set
The data sets are not assumed to be sorted or have the same number of points.
A graphical depiction is given for two data sets here:
Data Set B
Data Set A

## Slide 13: Association of XY points to XY points
The data sets are likely to have some points that are “mutual matches” where a pair of points in set A and set B are each the closest point to the point in the opposing data set.
The data sets are also likely to have points that do not have a close match once all of the mutual matches have been assigned.
Data Set B
Data Set A

## Slide 14: Nearest-neighbor or k-nearest-neighbor (kNN) searches are well-researched machine learning algorithms that can help determine mutual matches
  MATLAB implementation: [idx, dist] = knnsearch(datasetA, datasetB);
  The kNN search will return a vector of indices that indicate the nearest neighbor in datasetA to each point in datasetB.
  This can be modified to return a matrix of multiple (k) nearest neighbors for each point in datasetB.
  https://www.mathworks.com/help/stats/knnsearch.html
Requires: Statistics and Machine Learning Toolbox

## Slide 15: There may be points in set A that are the closest for multiple points in set B, or points that are never identified as a nearest neighbor.
Data Set B
Data Set A
Not a
neighbor
Duplicate
neighbor

## Slide 16: How the algorithm works
  Apply 1NN search to find the nearest neighbors in both directions
  Compare returned indices to determine which points have mutual matches
Data Set B
Data Set A
Data Set B
Data Set A
Data Set B
Data Set A
Data Set B
Data Set A

## Slide 17: How the algorithm works (continued)
  Check each mutual match the distance is less than a radial limit
  Reorganize (or copy) the matched points in Data Set A and Data Set B into a matrix where each row contains the X and Y coordinates of the two points
  Optionally, append each of the unmatched points in Data Set A with padding in the last two columns since there aren’t matches in Data Set B
  Optionally, append each of the unmatched points in Data Set B with padding in the first two columns since there aren’t matches in Data Set A
Data Set B
Data Set A
Data Set B
Data Set A

## Slide 18: Associated Data Statistics and Modifications

## Slide 19: It is useful to have some statistics for points in datasets that have been associated with each other
RMS Error: the RMS distances associated with the point-to-point match errors
Variance Error: the variance in the point-to-point match error distances
Mean Shift: the [X Y] shift that would cause the centroids of the two data sets to match
A function in the library helps us do this
Function: fcn_Points_calcPairStatistics.m
Script: script_test_fcn_Points_calcPairStatistics.m

## Slide 20: Another function allows us to modify the statistics of datasets by adjusting XY points
Function: fcn_Points_adjustPointSetStatistics.m
Script: script_test_fcn_Points_adjustPointSetStatistics.m

## Slide 21: Patches are used to represent objects that the vehicle can potentially collide into
Patches are represented as [1 x N] struct array in MATLAB
They are primarily defined by the x and y coordinates of their verticies inputted as two [M x 1] vectors for x and y, and a [1 x 3] RBG color vector.

## Slide 22: Sample patches are used to illustrate how patched are implemented in the library
Function: fcn_Patch_fillSamplePatches.m
Script: No script yet

## Slide 23: These patches can be easily visualized
Function: fcn_Patch_plotPatch.m
Script: script_test_fcn_Patch_plotPatch.m

## Slide 24: The library allows users to interactively create patches through color selection and mouse clicks
Function: fcn_Patch_fillPatchArrayViaUserInputs.m
Script: No script yet

## Slide 25: Axis Aligned Bounding Boxes (AABB), which are useful when working with collision detection, can be determined for each of the patches
Function: fcn_Patch_determineAABB.m
Script: script_test_fcn_Patch_determineAABB.m

## Slide 26: Basic Vehicle definitions

## Slide 27: We define the following vehicle properties
Body width
= Center of Gravity (CG)
CG-front bumper distance (df)
CG-rear bumper distance (dr)

## Slide 28: The heading angle is defined as the angle between the positive x axis and the heading (direction the vehicle is facing).
h0
Heading

## Slide 29: Slip angle is the angle between the vehicle’s velocity vector and the heading
Slip angle
Vehicle velocity
Heading

## Slide 30: The heading angle is defined as the angle between the positive x axis and the vehicle’s velocity vector
Course over ground
Vehicle velocity

## Slide 31: Construction Zones and Obstacles

## Slide 32: Construction work zones take various shapes, and tend to have various collidable objects on and near roads

## Slide 33: Common collidable objects found in construction sites are barrels, which from a top-down view can be modelled as regular octagon patches.
[istockphoto.com]
Function: fcn_Patch_fillBarrelAtPoint.m
Script: script_test_fcn_Patch_fillBarrelAtPoint.m

## Slide 34: A function in the library enables the finding of the inner and outer radius of circular trajectory that the vehicle can clear without collision
Function: fcn_Patch_CalcCircularTrajectoryGeometry.m
Script: script_test_fcn_Patch_CalcCircularTrajectoryGeometry.m
It also returns the tangent point (given by the *)
of the inner limiting radii

## Slide 35: Straight Path Collision Detection

## Slide 36: Finding the collision points between obstacles and a vehicle travelling down a straight path
Function: fcn_Patch_checkStraightCollisions.m
Script: script_test_fcn_Patch_checkStraightCollisions.m

## Slide 37: Important assumptions before we proceed to tackling the problem
We assume the collidable object to be in the shape of an arbitrary triangle
We assume the car to be approximated as a rectangle bounded by the maximum length and width of the car

## Slide 38: The strategy (explained in further details in upcoming slides)
Rotate (about CG) the vehicle and obstacles to point to the x-axis (to turn any situation into a standard problem) – use a rotation matrix
Use polyxpoly (matlab function to find intersection between two polylines) to find points of collision
We then check to see if there are any vertices of the object that lie on this rotated path
We then check to see if there have been any collisions by comparing the vertices and polyxpoly intersection points
collVertexInds = find(abs(rotObst(:,2)) < 1*vehicle.w/2 & rotObst(:,1) > -vehicle.dr);

## Slide 39: Rotate (about CG) the vehicle and obstacles to point to the x-axis (to turn any situation into a standard problem) – use a rotation matrix

## Slide 40: Use polyxpoly (matlab function to find intersection between two polylines) to find points of collision
We determine any obstacles that lie within or across the vehicle path on the positive the x-axis between the back of the vehicle (-vehicle.dr) and some large distance (1e6) (this area is given by the red box)
Link to polyxpoly documentation: https://www.mathworks.com/help/map/ref/polyxpoly.html
Potential collision
Potential collision
Potential collision
Potential collision

## Slide 41: We then check to see if there are any vertices of the object that lie on this rotated path
collVertexInds = find(abs(rotObst(:,2)) < 1*vehicle.w/2 & rotObst(:,1) > -vehicle.dr);
Checking within the width of the vehicle
Checking between x-axis between back of vehicle and come large distance

## Slide 42: We then check to see if there have been any collisions by comparing the points we obtained before
If there is a collision, we compare whether the vertex was closer or polyxpoly point is closer. Which ever point is closer is the collision point.
If there is no collision, we try to find the minimum clearance and location of this on the obstacle.
Closest point -> point of collision

## Slide 43: Once this point is obtained, we rotate and translate it back to the original coordinate space
*
*
Collision point

## Slide 44: There are several test cases that the algorithm can encounter
Collision with right edge
Collision with left edge
Collision with multiple objects’ edges

## Slide 45
Collision with vertex
Collision with multiple objects’ vertex

## Slide 46: The algorithm displays the location of the minimum clearances on the figure as near misses

## Slide 47: We can also have these different test cases plotted as a single scenario

## Slide 48: Curved Path Collision Detection

## Slide 49: Finding the collision between a objects and a vehicle travelling down a curved patch
Something important to note is that a straight path is considered to be a curved path with an infinite radius, so any path can be treated as a curved path.
However, we consider the straight path to be a special case and use fcn_Patch_checkStraightCollisions.m for that case
Function: fcn_Patch_checkCollisions.m
Script: script_test_fcn_Patch_checkCollisions.m

## Slide 50: The strategy (explained in further details in upcoming slides)
Define pertinent radii and calculate center of path radius circle
Convert from vehicle body coordinates to inertial coordinates using a rotation matrix
Checking to find intersection points between vehicle vertex and object edge
Checking to find intersection points object vertex and vehicle edge
Checking for collision by comparing obtained intersection points or calculating near misses

## Slide 51: Vehicle trajectory for a curved path is defined by several pertinent radii

## Slide 52: They are calculated as follows:
CG (circle) and CG path (black dash-dot line)
Front left and front right corner paths (gray lines)
Maximum clearance radius (blue line)
Minimum clearance radius (red line)
a

## Slide 53: We changes the frame of reference to inertial coordinates with respect to the car by defining a rotation matrix (To be completed)
Rotation matrix = [cos(K) sin(K)
-sin(K) cos(K)]
K = initial course over ground (rad) + slip angle (rad) (in vehicle body coordinates)

## Slide 54: Checking to find intersection points between vehicle vertex and object edge (To be completed)

## Slide 55: Checking to find intersection points object vertex and vehicle edge (To be completed)

## Slide 56: Checking for collision by comparing obtained intersection points or calculating near misses (To be completed)

## Slide 57
Considering all the possible collision/near miss possibilities
 | Front of Car | Inside of Car | Outside of Car
Vertex within track width | Direct calculation of vertex angle relative to center | N/A | N/A
Vertex between inside front corner and min radius | N/A | Calculate distance ahead of CG for collision then offset from vertex angle | N/A
Vertex between outside front corner and max radius | N/A | N/A | Calculate distance behind CG for collision then offset from vertex angle
Edge entirely within track width | Handled by vertex checks | N/A | N/A
Edge between min radius and track width | Handled by vertex check if track width vertex comes first | Circle/edge intersection check with inside front | N/A
Edge between max radius and track width | Handled by vertex check if track width vertex comes first | N/A | Circle/edge intersection check with outside front
Edge spans the track width but vertices within min and max radii | N/A unless edge is perfectly parallel to front of car | Circle/edge intersection check with inside front | Circle/edge intersection check with outside front
Edge spans min and max radii | N/A unless edge is perfectly parallel to front of car | Circle/edge intersection check with inside front | Circle/edge intersection check with outside front
Edge spans max radius with vertex outside of outer front track radius | N/A | N/A | Circle/edge intersection check with outside rear OR vertex check behind CG (depends on edge angle)
Edge spans min radius with vertex outside of inner front track radius | N/A | Vertex check ahead of CG | N/A
Vertices outside max/min radii (near miss) | N/A | Determine point with minimum difference from CG radius by vertices | Determine point with minimum difference from CG radius by vertices and nearest point on edges.

## Slide 58: Vertex/vertices within track width

## Slide 59: Vertex between inside front corner and min radius

## Slide 60: Vertex between outside front corner and max radius

## Slide 61: Edge entirely within track width

## Slide 62: Edge between min radius and track width

## Slide 63: Edge between max radius and track width

## Slide 64: Edge spans the track width but vertices within min and max radii

## Slide 65: Edge spans min and max radii

## Slide 66: Edge spans max radius with vertex outside of outer front track radius

## Slide 67: Edge spans min radius with vertex outside of inner front track radius

## Slide 68: Vertices outside max/min radii (near miss)

## Slide 69: References
https://www.freepik.com/free-vector/set-construction-site-objects_27285642.htm
https://www.istockphoto.com/photos/road-construction-barrels
https://www.wired.com/2017/02/self-driving-cars-cant-even-construction-zones/